## Slide 1: template-based stereo odometry
Alankar Kotwal
Indian Institute of Technology Bombay
alankarkotwal13@gmail.com

## Slide 2: defining the problem
with the stereo camera
facing the floor
figure out how the
camera moved
wrt the floor

## Slide 3: why is this difficult?
unique feature points (corners)
in normal images
no corners or too much
self-similarity => false matches!

## Slide 5: why stereo?
sense of scale absent
in monocular systems
=> need to use ultrasonics /
other rangefinders
narrow field of view
better to track two images?
possibilities of getting
more information?

## Slide 6: can we make a better ;) replacement?

## Slide 7: clearly, we can’t use feature points

## Slide 8: which means we need to use direct matching
SSD / SAD / Normalised Cross-Correlation

## Slide 9: general workflow
get stereo disparity
get stereo depth
(maybe roll, pitch?)
get frame-to-frame
optical flow
convert flow to physical
displacement and
rotation

## Slide 10: (rectified) stereo disparity
assumption: plane nearly
parallel to camera planes
assumption: camera pose
doesn’t change
much between frames
displacement only in this direction

## Slide 11: estimate disparity by measuring translations!
translations by maximising NCC, here

## Slide 12: why not regular stereo-matching?
big correlation window size => slow, bad results

## Slide 13: disparity -> depth
known camera parameters

## Slide 16
PX4FLOW

## Slide 17
DUO3D

## Slide 18: outliers and angles?
planar assumption => looking
only at the floor!
non-planar case is hard!
which areas to track?
camera tilted? some ideas later

## Slide 19: position tracking
considering our almost-level assumption,
scale, rotation and translation

## Slide 20: s-r-t tracking: try 1
scale from depths for
this and initial frame
rescale initial frame to
fit current frame
assume rotation isn’t
much, get translation
(NCC as in stereo!)
try to get rotation by
maximizing NCC for
rotated template

## Slide 21: results
without rotation, good estimates of 3-d coordinates

## Slide 22: s-r-t tracking: try 2
gradient-descent
s-r-t tracker
ViSP
vpTemplateTracker class
to track images across time
vpTemplateTrackerWarpSRT

## Slide 23: more results
excellent estimates of 3-d coordinates and yaw!
see ahead..

## Slide 24: making this robust

## Slide 25: depth: block matching
run outlier rejection to get robust displacement

## Slide 26: but this gives us more!
what if we fit a model to the depth variation?

## Slide 27: RANSAC plane-fitting
get depths by block
matching
get world coordinates
of block centers
fit plane using outlier
rejection
get roll, pitch!

## Slide 29: we have 6-DoF!
and, this takes care of the slightly non-planar case

## Slide 30: of course, conditions apply
sufficient lighting, texture for the difference measure
unreliable at the moment

## Slide 31: ROS implementation details
master
stereo driver
tracker
parameters
parameters
image_rect
CameraInfo
/tracker/
x
y
tracker_z
stereo_z
yaw
roll
pitch

## Slide 32: data fidelity
histogram of recorded displacements over 20 cm length
wooden table-top

## Slide 33: data fidelity
histogram of recorded yaws over 90 deg
wooden table-top

## Slide 34: data fidelity
typical unwrapped yaw over five rotations
wooden floor

## Slide 35: drifts
typical stationary position drift, at 50cm, wooden table-top
RMS
drift

## Slide 36: drifts
typical stationary yaw drift, at 50 cm, wooden table-top
RMS
drift

## Slide 37: stress-tests on depth, 1s
~ 5 cm, with enough light
~ 1 m
use ultrasonics for
better heights?

## Slide 38: stress-tests on speed
resolution | max x-speed | max angular speed
1x | ~ 0.18 m/s | ~ 10 deg/s
0.5x | ~ 0.3 m/s | ~ 15 deg/s
0.3x | ~ 0.4 m/s | ~ 15 deg/s
0.25x | ~ 0.4 m/s | ~ 20 deg/s
approximate best values, wood floor

## Slide 39: notes
works best on textured surfaces
white tiles are bad!
good lighting a must!
specularities are BAD!
honour speed limits!
as of now, camera needs to be nearly horizontal

## Slide 40: long-range test: corridor
*if you do this slow enough and follow all conditions above*
textured carpet
5 m
75 m
position drift over loop ~ 30 cm
yaw drift over loop ~ 30 deg
height 20-50 cm

## Slide 41: advantages over PX4FLOW?

## Slide 42: better depth estimates
as in the graph, lower depths and more reliability

## Slide 43: (potentially) better maximum camera speeds
better field of view, see ahead..

## Slide 44: PX4FLOW vs DUO: speed
PX4FLOW max ground
speed ~ 0.25 m/s
tested at
~ 0.3 - 0.4 m/s
max vertical speed
~ 0.1 m/s
no limits
(absolute measurement)
ref.: http://diydrones.com/profiles/blogs/px4flow-microquad-adventure
rotation speed ~ 10 deg/s
?

## Slide 45: no dependence on external hardware
no gyro needed, unlike PX4FLOW

## Slide 46: disadvantages

## Slide 47: slow processing, @ ~ 3Hz
mostly because of depth-determination
better tracking algorithm? see ahead..

## Slide 48: override: downsampling
almost as reliable results with 0.5, four times faster!
(greater drifts, of course)

## Slide 49: other things tried
which didn’t go as well ;)

## Slide 50: affine / projective transforms for depth
unreliable homography fits, slow affine fits
problems due to inadequate rectification

## Slide 51: homographs for depth
ref.: http://web.eecs.umich.edu/~jjcorso/pubs/jcorsoreport2002.pdf
rectified images =>
=>

## Slide 52: affine homographs
approximate homography by affine transform?

## Slide 53: we could use the above for position too!

## Slide 54: what I didn’t do
(but would like to)

## Slide 55: making position estimation robust
similar block-matching with an s-r-t warp
RANSAC-based filtering

## Slide 56: keyframes
to eliminate long-term drift

## Slide 57: hardware acceleration
to allow greater frame-rates, speeds

## Slide 58: the badly non-planar case
identify 'connected' regions by edge detection
and then track them individually?

## Slide 59: fusing depth data
from the position tracker, stereo and ultrasonics
(tracker good at high freq, others good at low freq)

## Slide 60: thank you