## Slide 1: Joint Desmoking and Denoising of Laparoscopy Images
Alankar Kotwal1 , Riddhish Bhalodia1 , Suyash P. Awate2
1Electrical Engineering Department
2Computer Science and Engineering Department
Indian Institute of Technology (IIT) Bombay
Notes: Good afternoon everyone today I will be talking about
So let’s get on with the presentation I hope that I don’t bore you to sleep in this after lunch session
Also as we are talking about surgery there are graphic images and videos

## Slide 2: Overview
Background and Motivation
Prior Art
Observations and Approach
Results
Notes: Hello
I am Riddhish Bhalodia
I along with Alankar Kotwal have been working on the problem of laparoscopy image enhancement under the supervision of Prof. Suyash Awate
So let’s get on with the presentation I hope that I don’t bore you to sleep in this after lunch session
12 mins

## Slide 3: Laparoscopy
Minimally Invasive surgery
Onscreen viewing through inserted camera
Smaller incisions
Less pain, hemorrhaging, drastic reduction in recovery time
Source : Wikipedia
Notes: A little introduction about laparoscopy
Also known as minimally invasive surgery
The idea is to replace big incisions required for open surgery by smaller holes to insert the camera and instruments
The surgen views the procedure on a screen
This drastically reduces the recovery times and also reduces complication like heomorraging and infections
No Scars

## Slide 4: Surgical Smoke
By electro-cauterization
Accumulates and causes visibility loss
Notes: Surgical smoke is mainly caused by electrocauterization, which is used for suturing wounds or cutting tissues The smoke accumulates as the surgery progresses.
We can see it in this video
Currently the surgeons usually remove all the instruments and suck out the smoke by vaccum pump, this cause the loss of valuable surgery time
That brings us for the motivation to have a software solution for laparoscopic desmoking

## Slide 5: Motivation
Improvement in visibility
Reduces risk
Reduces surgery time
Pre-processing step to improve accuracy of many medical vision algorithms
Notes: Improvement in the visibibility
It reduces risk which comes with visibility loss at times
Reduces surgery time as you do not have to remove the smoke everytime
It will improve the accuracy of several medical robotic techniques like organ segmentaion/ identificatin and instrument tracking if we us ethis as a pre-processing step

## Slide 6: Prior Art
To the best of our knowledge there exists no laparoscopic desmoking algorithm in current literature
Dark Channel Prior based Dehazing methods [He et al 2009 CVPR]
Does not have Bayesian Formulation
Provide no contextual information about the image
Bayesian Defogging [Nishino et al 2012 IJCV]
No prior on color channels only on chromaticity
Unnatural color and brightness variation
Adaptive filtering using Wiener filter [Gibson et al. 2013 ICIP]
Does not employ edge-preserving prior models on the transmission map or the uncorrupted image
Notes: As per our information there has been no work done in the field of laparoscopic demoking
So in this work we compare our method with the existing dehazing methods for landscape images
Like bayesina defogging
Dark channel prior and
Adaptive filering

## Slide 7: Smoke Image Model
Yi – Output corrupted image
Xi – Uncorrupted image
Ti – Transmission map, attenuation of intensity due to scattering
S – Global diffused light (Corruption Color), due to diffused scattering
ηi – Additive i.i.d zero mean Gaussian noise

## Slide 8: Our Approach
Bayesian inference problem (MAP estimation)
LIKELIHOOD
PRIOR
INDEPENDENT PRIOR MODELS
Due to zero mean i.i.d. additive Gaussian noise
Notes: We formulate a MAP estimation prblem as follows
Split it into the likelihood term and prioir on the uncorrupted image and the transmission map
We also assume that these priors are independent
Due to the iid additive Gaussiona Noise
We get the likelihood as follows

## Slide 9: Prior Model on Transmission Map (T)
Edge preserving smoothness MRF
: Huber Function
Notes: T : We model the estimated transmission map as a piecewise smooth function and hence we impose an edge-preserving MRF on T as follows, the gibbs energy is given as L1 norm regularized by huber function and W is the partition function

## Slide 10
Histograms of non-smoky laparoscopic images
  Can be fitted with Gamma Distributions
  Very small variation across images
Prior on Uncorrupted Image (X)
Notes: The key observation is that when we plot the histograms of abiut 50 clean (no smoky images) chosen at random we can fit each channel very well with a gamma distribution
And this fitted gamma distributions does not vary much on addign or removing more images
We will use this imformation to develo a prioir model for image estimation

## Slide 11: Prior on Uncorrupted Image (X)
Edge preserving smoothness term
Divergence from learned Gamma distributions
KS : Kolmogorov-Smirnov distance
Notes: The prior on the uncorrupted image X have two terms, one corrosponds to the standard edge preserving smoothness term as described, it is imporsed as the estimate of X must be piecewise smooth.
The second term is where we use the observation done on the histograms of the laparoscopy histograms, we penalize the deviation of the CDF of the estimated image and the learned gamma prioirs by using KS divergence as MRF potential function on the fully connected neighbourhood system on each color channel. F_RGB are the CDF of the image estimate at that time.

## Slide 12: Corruption Color (S) Estimation
Estimate S beforehand
  Robustly construct ‘smokiness map’ of pixels having similar colors in all three channels
  Select the pixels with intensity values in bottom 1 percentile of the ‘smokiness map’
  Project on 1D subspace learned on training data
  Project the estimated S on this learned subspace for added robustness
Notes: The S estimation is done through a hueristic.
We construct the smokiness map
We take the corrupted image data
y
(Figure 2(a))
and automatically select regions with colors that are (i) homo-
geneous and (ii) close to a gray shade, i.e., similar RGB color
components. We do this by constructing a grayscale image
called the
smokiness map
(Figure 2(b)) as follows: (i) com-
pute the standard deviation (SD) of the 3 color-component
values at each pixel, (ii) set the intensity at pixel
I to the 95-th percentile of these SD values in its
Neighborhood
Average value of the ottom 1 percentile pixels of the smokiness map and that will be the s hat
We estimate such s hat from several images and the can be projected onto a 1D subspace.
Then all the estimates are projected onto this subspace for added robustness

## Slide 13: Optimization
We estimate the corruption color (S)
Perform gradient descent with alternate minimization over X and T
~15-20 Iterations
Notes: Using the following the previous slides we use gradient descent with adaptive step size as the optimization algorithm
For the gradient of the KS divergence of the prioir term we use the CDF penelty by performing histogram matchning

## Slide 14: Validation: Simulated Images
X : piecewise-constant image
S : constant
T: Transmission map
Noise i.i.d. Gaussian with 𝜎2
Original
Smoky
Corruption Color
Transmission Map
Notes: Results
We constructed a phantom image and added the simulated noise and haze and then erformed the evaluations

## Slide 15: Validation: Simulated Images
Original
Smoke with low noise
Our Result
Adaptive Filtering Result
[Gibson et al 2013 ICIP]
Dark Channel Dehazing +
Denoising Results
[He et al 2009 CVPR]
Smoke with high noise
Notes: Pointer Needed
Original
High haze low noise 0.01 = sigma
Our method
Adaptive denoising
Denoising followed by dark channel dehazing
For the high noise case

## Slide 16: Validation: Simulated Images
Boxplots for 5 different smoke and noise levels
Notes: Quantitative comparision between the different approaches
For different levels of haze and noise

## Slide 17: Validation: Simulated Smoke on Real Images
X : real-world laparoscopy image
S : constant
T: Transmission map
Noise i.i.d. Gaussian with 𝜎2
Corruption Color
Transmission Map
Smoky
Original
Notes: We took clean laparoscopic images and then added simulated noise and haze

## Slide 18: Validation: Simulated Smoke on Real Images
Original
Our Result
Adaptive Filtering Result
[Gibson et al 2013 ICIP]
Dark Channel Dehazing +
Denoising Results
[He et al 2009 CVPR]
Smoke with low noise
Smoke with high noise
Notes: Preserves the naturalness better then other dehazing methods

## Slide 19: Validation: Simulated Smoke on Real Images
Boxplots for 5 different smoke and noise levels, for 10 images
Notes: Also mention about the sensitivity testing

## Slide 20: Results on Real Images
Original
Wiener
Filter
Dark
Channel
Prior
Our
result
Notes: Visual comarision also shows our method to be significantly better than the others specifically for the laparoscopic images

## Slide 21: Video Result
Our Output
Real Video Clip

## Slide 22: Clinical Evaluation
Blind evaluation by 4 independent experts
Rating every processed image on {1, 2, …, 5}
Method | Mode | Median | Mean | Standard Deviation
Proposed | 5 | 5 | 4.4 | 0.8
Dehazing + Denoising | 3 | 3 | 3.1 | 0.8
Notes: Did a clinical evaluation with 4 different laparoscopic surgeons and they were required to score 30 images with the score between 1-5
And these are the results

## Slide 23: Thank You
Riddhish Bhalodia: riddhishb@gmail.com , Alankar Kotwal: alankarkotwal13@gmail.com , Suyash Awate : suyash@cse.iitb.ac.in
Thanks: IIT Bombay Seed Grant 14IRCCSG010